## Slide 1
Regional quantification of rock glacier movement in Austria using governmental GIS data
V. Kaufmann Institute of Geodesy Working Group Remote Sensing and Photogrammetry Graz University of Technology, Austria A. Kellerer-Pirklbauer Department of Geography and Regional Science University of Graz, Austria E-mail: viktor.kaufmann@tugraz.at http://www.geoimaging.tugraz.at/viktor.kaufmann/

## Slide 2: Regional quantification of rock glacier movement in Austria using governmental GIS data
1. Introduction
Kinematics of rock glaciers
Application of geobrowsers (Google Maps, Microsoft Bing) for detection and quantification of fast moving rock glaciers
Study area: Schober Mountains (Hohe Tauern Range, Austria)
Hohe Tauern Range
Schober Mountains

## Slide 3: Regional quantification of rock glacier movement in Austria using governmental GIS data
Study area: 125 km2

## Slide 4: Regional quantification of rock glacier movement in Austria using governmental GIS data

## Slide 5: Regional quantification of rock glacier movement in Austria using governmental GIS data

## Slide 6: Regional quantification of rock glacier movement in Austria using governmental GIS data
2. Multi-temporal digital orthophotos
Date | Original GSD (cm) | Spectral bands | Type of camera
Sept. 18, 2002 | 25 | RGB | Analog
Sept. 7, 2009 | 25 | RGB | Analog
Aug. 25, 2012 | 20 | RGB NIR | Digital
GIS data providers: Regional government of Tyrol (TIRIS – https://www.tirol.gv.at/statistik-budget/tiris/) Regional government of Carinthia ( KAGIS – http://www.kagis.ktn.gv.at/)

## Slide 7: Regional quantification of rock glacier movement in Austria using governmental GIS data
3. Visual detection of surface change
Animated GIF: 2002 – 2009 – 2012
Tschadinhorn rock glacier
50 m

## Slide 8: Regional quantification of rock glacier movement in Austria using governmental GIS data
3. Visual detection of surface change
Snout of Tschadinhorn rock glacier
August 1, 2014

## Slide 9: Regional quantification of rock glacier movement in Austria using governmental GIS data
4. Computation of displacement vectors and flow velocity
Matlab-based program
Change detection (multi-temporal orthophotos and DEMs)
Image matching (NCC, back-matching)
Sub-pixel accuracy
Automatic detection of outliers
Stable areas: detection of small systematic offsets, accuracy assessment

## Slide 10: Regional quantification of rock glacier movement in Austria using governmental GIS data
5. Results
Two thematic maps (2002-2009, 2009-2012) showing the mean annual horizontal flow velocity of all rock glaciers of the study area
12 intact rock glaciers revealed significant movements in both periods.
Vmax = 440 cm/a
Velocity increase by a factor of 1.4 to 1.8

## Slide 11: Regional quantification of rock glacier movement in Austria using governmental GIS data
GSD = 50 cm

## Slide 12: Regional quantification of rock glacier movement in Austria using governmental GIS data
Tschadinhorn rock glacier
GSD = 20 cm

## Slide 13: Regional quantification of rock glacier movement in Austria using governmental GIS data
Tschadinhorn rock glacier
max. flow velocity = 117 cm/a
max. flow velocity = 177 cm/a

## Slide 14: Regional quantification of rock glacier movement in Austria using governmental GIS data
6. Conclusions
Data availability and accuracy
  Multi-temporal orthophotos (3-year interval) are available.
  Geometric quality of orthophotos is generally high.
  Relative registration error of ±60 cm for any two orthophotos, thus
  3-year interval: accuracy is approx. ±20 cm/a;
  The detection of slow moving rock glaciers is not possible.
  Ortho-rectification quality is mainly influenced by DEM.
  The current availability of multi-temporal governmental DEMs is limited.
  DEMs offer great potential in change detection.

## Slide 15: Regional quantification of rock glacier movement in Austria using governmental GIS data
6. Conclusions
Rock glacier speed-up and climate relationship
  Almost all fast moving rock glaciers in the study area have increased their mean annual flow velocities.
  This regional signal is also confirmed on an Alpine-wide scale.
  Warmer temperatures favor higher velocities.

## Slide 16: Regional quantification of rock glacier movement in Austria using governmental GIS data
For further information, please contact: Viktor Kaufmann Institute of Geodesy Working Group Remote Sensing and Photogrammetry Graz University of Technology Steyrergasse 30 A-8010 Graz, Austria E-mail: viktor.kaufmann@tugraz.at http://www.geoimaging.tugraz.at/viktor.kaufmann/